## Slide 1: Chapter 11 Routing Protocols
Interior and exterior routing
Distance vector routing & RIP
Link state routing & OSPF
Path vector routing & BGP-4
Notes: 路由协议
域内和域间路由
距离向量路由，链路状态路由 路径向量路由

## Slide 2: Introduction
Routing Table
  Static route  manually define
  Dynamic route  routing protocol
Table-driven routing 表驱动路由
  One router  More routed protocols
  One routed protocol  One routing table
  One routed protocol  More routing protocols
  每个路由的协议可以生成多个协议
Routing protocol
  To share the knowledge about the internet共享对网络的掌握状况
  To calculate the routing table based on the topology or the policies
Convergence
Overhead
Scalability
Notes: 生成路由表的特征：收敛，成本，可扩展

## Slide 3: Metric（度量）
Information used by a routing protocol to select the best path for routing
  The total metric of a route = the sum of the metrics of networks that comprise the route
  A router chooses the route with the shortest metric
Factors
  Hop count跳数, bandwidth带宽, delay延迟（传播/传输）, MTU（最大传输单元）, load负载, reliability可用性, …电量（无线的度量）
  Routing protocols can use one or more different factors to calculate a metric
A
D
C
B
Net
64K
64K
10M
10M
10M
Hop count: A  B  Net
Bandwidth: A  C  D  Net
Notes: 几种路由协议的三个指标和比较 定性和定量分析：为什么Ospf快，经过多少节点 必考***********

## Slide 4: Convergence（收敛）
Convergence
  All routers in a network agree on the topology
Convergence time
  A measure of how quickly to recover from network changes
Factors affecting convergence
  The routing protocol used
  A router’s distance from the point of change
  The number of routers in the network
  Bandwidth and traffic load on communications links
  A router’s load
  Traffic patterns in relation to the topology change

## Slide 5: 11.1 Interior & Exterior Routing
Autonomous system（自治系统，AS）
  A group of networks and routers under the authority of a single administration
  Each AS typically represents an independent organization and applies its own unique routing and security policies
AS number
  An identifying number that is assigned by an Internet registry or a service provide
  Range: 1~65535
  Private AS number: 64512~65535

## Slide 6: IGP vs. EGP
IGP: Interior Gateway Protocol（内部网关协议）
  To be used within an autonomous system
  To find the best path to the network
  Example：RIP、OSPF、IS-IS
EGP: Exterior Gateway Protocol（外部网关协议）
  To be used between autonomous systems
  To find the best path to the AS
  Example：BGP-4
Note
  The static routing or an IGP could also be used between autonomous systems in some case
AS1
AS2
R
R
EGP
IGP
IGP

## Slide 7: Routing Protocols
Routing protocols
  Concept of the routing method
  Features and messages
  Operation
Protocol | Type | Routing method | Popular ver.
RIP | IGP | Distance vector routing | RIPv1, RIPv2
OSPF | IGP | Link state routing | OSPFv2
BGP | EGP | Path vector routing | BGP4

## Slide 8: 11.2 Distance Vector Routing
Initialization
  Directed routes: directed network & metric
Sharing the knowledge about the internet
  What the routing table – network & metric
  Where only with the immediate neighbors
  When periodical & triggered
Updating the routing table
提供了指向网络的路标 ！

## Slide 9: Updating
A
D
C
B
E
3
2
5
4
4
3
①
③
②

## Slide 10: Routing Loop: Two-node instability
Net 1
Net 2
Net 3
Net1 |  | 
…… | … | …
Routing table
Net1 |  | A
…… | … | …
Routing table
A
B
You can reach net1 through me with length 2
B can reach net1 ! Great !
Hop count changed !
-
1
16
2
3
Hop count changed !
4
-
B
∞
∞
B: ( net1, 2 )
A: ( net1, 3 )
B: ( net1, 4 )

## Slide 11: Some Remedies for Instability
Defining infinity（定义无穷大）
  Use a finite metric value to represent "infinity“
    The value must be large enough that no real metric would ever get that large
Triggered update（触发更新）
Split horizons（水平分割）
Poison reverse（毒性逆转）
  A variation of split horizons
None of them are 100% effective !

## Slide 13: (2)Triggered Update
An attempt to speed up the convergence
  If there are no changes on the network
    To send update messages at usual 30-s intervals
  If there is a change
    To send update messages almost immediately
Special handling in RIP
  To limit the frequency of triggered updates
    Set a timer for a random time between 1 and 5 s
    A single update is triggered when the timer expires
  To limit the routes included in triggered updates
    At least those changed routes

## Slide 14: (3)Split Horizons
Net 1
Net 2
Net 3
A
B
Net2 1
Net3 2
Net1 1
RIP messages
Net1 2
Net2 1
Net3 1
RIP messages
Notes: 分割范围，只交换 该端口之外的连接信息，如路由器A给B的信息只有Net1 1

## Slide 15: (4)Poison Reverse
Net 1
Net 2
Net 3
A
B
Net2 1
Net3 2
RIP messages
Net1 16
Net2 16
Net3 16
Net1 1
RIP messages
Net2 16
Net3 1
Net1 16
Net2 1
Net3 16
Net1 2
Disadvantage:
Increasing the size of
the routing messages
Notes: 一直删除某端口的信息，会造成 该节点链路断开 与 分割范围机制的混淆，因此加入 Poison Reverse机制，将交换信息的本端口反向度量设置为无穷大(usually 16),”不要使用这个数值，因为我所知道的数值来源于你”

## Slide 16: More-node instability
1. Net 1 unreachable, then E sends a triggered
update to its neighbor A
2. Then A knows Net 1 is unreachable from E,
then sends a triggered update only to neighbors
B and D because of the split horizons
3. B and D know Net unreachable from A, then send a triggered update only to the neighbor C because of the split horizons
4. Assume that C has known about Net 1 from B, and C sends a regular update about Net 1 is accessible to D before the triggered update has been received.
5. Then D think Net 1 can be reachable through C, so D updates its routing table and informs A  routing loop
Net 1
A
B
C
D
E

## Slide 17: Hold-down Timer, 抑制定时器
To prevent update messages from reinstating inaccessible routes —— not in RFC
  When a router receives an update that indicates a network is unreachable, it starts a hold-down timer ( 180 s )
  While the hold-down timer is running, the router will NOT accept any update about the inaccessible route UNLESS
    the update comes from the originator of the previously inaccessible update
    or from a router reporting a better metric to the inaccessible network
Notes: 1.更新计时器（update）：30S更新路由表；2.无效计时器（invalid）：180S不刷新则将该路由条目的度量值设置为16；
3.刷新计时器（flush）：默认240S，比无效计时器长60S，刷新后路由条目则删除；4.抑制计时器（Hold-down）：180S。

## Slide 18: 11.3 RIP
Routing Information Protocol，RIP
  v1：RFC 1058，v2：RFC 2453，路由信息协议
IP
LANs
MANs
WANs
ICMP
IGMP
ARP
RARP
Network
Layer
Network
Access Layer
TCP
UDP
Transport
Layer
RIP
Application
Layer
520
软件实现层次
RIP = RIPv1
Notes: RIP(Routing Information Protocol，选路信息协议)是一个应用层协议，基于UDP，端口号为520

## Slide 19: Example of a domain using RIP
Metric: hop count（跳数）
Infinity = 16, means unreachable
The maximum hop count = 15
Notes: Hops个数，也意味着delivery次数，无穷大被定义为16，则最大跳数不能超过15

## Slide 20: 11.3.1 RIP Message
Format ( <=512 bytes )
Encapsulation: UDP ( port 520 )
Command
Version
IP address
All 0s
All 0s
All 0s
Metric ( hop count )
All 0s
Family = 2
Repeated
Notes: 命令字段指明报文类型，请求(1)或响应(2)，RFC中原本还有3 4 已被废弃不用，5用于Sun Microsystems， 8bits版本号，目前有2个版本 V1和V2，本章讨论V1，family/系列，2为TCP/IP，14个字节的网络地址，目前只用到 IP address4字节，Metrics为hops，该表格称为1个表项entry

## Slide 21: Types of Messages
Request ( Command = 1 ): broadcast
  All entries ( IP address = 0.0.0.0 )
    To be sent by a router that has just come up
  Specific entries ( IP address ≠ 0.0.0.0 )
    To be sent by a router that has some time-out entries
Response ( Command = 2 )
  Solicited: unicast to the asker
    To be sent only in answer to a request
  Unsolicited: broadcast to every neighbor
    To be sent every 30 s, contain the entire routing table
Notes: 特定项目请求/所有项目请求， 询问的响应，非询问响应

## Slide 22: 11.3.2 RIP Operation
Discovery
Topology change
Calculating
  RIP updating algorithm
Initialize
RT
Send
RT
Update RT
Update?
Send RT per 30s
No
Yes
Find the change
Update
RT
Send RT
on schedule
Like discovery
Split horizons & poison reverse
Triggered update
Notes: 发现

## Slide 23: Initializing the Routing Table
Only the directly attached networks
  RFC 1058: metric = 1
  In most routers: metric = 0
Examples of some router’s routing table
  Cisco router
  C 10.1.1.0 is directly connected, FastEthernet0/0
  华为 router
  Dst/Mask Proto Pref Metric Nexthop Interface
  10.1.1.0/24 Direct 0 0 10.1.1.254 Ethernet0
……
……
RFC 1058: section 3.6
Notes: 本地局域网10.1.1.0 ，Pref 用于多路由协议中的优先级，值越小则优先级越高，0表示直接路由

## Slide 24: RFC 1058: Sending RIP Responses
Source IP address
  The IP address of the sending interface
  Consider: multiple IP addresses on a single physical interface
The entries
  Answer to a request: the requested routes
  Regular update: the whole routing table
  Triggered update: only the changed routes
  Note: the max datagram size is 512 bytes
In each entry
  Address: host addr, subnet addr, network addr, 0.0.0.0
  Metric: from the routing table without change
Notes: RFC 1058: section 3.4.2，“在路由设置两个虚拟接口192.168.0.1(/24)及192.168.1.1(/24)如果从192.168.0.0网络访问路由器该路由的主接口就是192.168.0.1,如果通过192.168.1.0网络访问该路由器,该路由器的主接口为192.168.1.1”

## Slide 25: RFC 1058: Updating the Routing Table
When receive a response RIP message
First to check for validity
  Port number, source IP address
Then to process the entries in it one by one
  1. Ignore the entry whose metric, address or unused fields are invalid
  2. Update the entry’s metric = min ( metric + 1, 16 )
  3. If the entry address is not in the RT, then add it
  4. Else if the next-hop in the RT is same with source IP address, then replace the route in the RT with this entry
  5. Else if the new metric is lower than the one in the RT, then replace the route in the RT with this entry
Notes: 记住Update the entry’s metric = min ( metric + 1, 16 )

## Slide 26
RFC1058：
发送时 unchanged
接收时 Metric + 1
某些实现：
发送时 Metric + 1
接收时 unchanged

## Slide 27: Network Discovery
A
B
C
N1
N2
N3
N4
1
2
1
2
1
2
N3 | - | 1 | 0
N4 | - | 2 | 0
N1 | - | 1 | 0
N2 | - | 2 | 0
N2 | - | 1 | 0
N3 | - | 2 | 0
路由表：
目的网络 | 下一跳 | 发送接口 | Metric


N3
N1
N2
B1
2
1
A2
1
1
B2
1
1
C1
2
1
N4
A: (N1, 1) (N2, 1)
B: (N2, 1) (N3, 1)
C: (N3, 1) (N4, 1)
B: (N2, 1) (N3, 1)


N4
B1
2
2
N1
B2
1
2
A: (N1,1) (N2,1) (N3,2)
B: (N2,1) (N3,1)
(N1,2) (N4,2)
C: (N3,1) (N4,1) (N2,2)
B: (N2,1) (N3,1)
(N1,2) (N4,2)


A:(N1,1)(N2,1)(N3,2)(N4,3)
B: (N2,1) (N3,1)
(N1,2) (N4,2)
C:(N3,1)(N4,1)(N2,2)(N1,2)
B: (N2,1) (N3,1)
(N1,2) (N4,2)

## Slide 28: Topology Change
A
B
C
N1
N2
N3
N4
1
2
1
2
1
2
N3 | - | 1 | 0
N4 | - | 2 | 0
N1 | - | 1 | 0
N2 | - | 2 | 
N2 | - | 1 | 
N3 | - | 2 | 0


N3
N1
N2
B1
2
1
A2
1
1
B2
1
1
C1
2
1
N4

N4
B1
2
2
N1
B2
1
2
B: (N2,16) (N3,1)
(N1,16) (N4,2)
A: (N1,1) (N2,16)
(N3,16) (N4,16)
0
0
∞
∞
∞
C: (N3,1) (N4,1)
(N2,16) (N1,16)
∞
∞
∞
∞

## Slide 29: 11.3.3 Timers in RIP
Timers
Garbage collection
120 s
(for each route)
Expiration
180 s
(for each route)
Periodic
30 s
(for each router)
E = 180 s
E = 180 s
Metric 16
G = 120 s
25~35 s
180 s
删除
路由
120 s
实现中：
P＝25 ~ 30 s
G＝60 or 120 s
Notes: 1.更新计时器（update）：30S更新路由表；2.无效计时器（invalid）：180S不刷新则将该路由条目的度量值设置为16；
3.刷新计时器（flush）：默认240S，比无效计时器长60S，刷新后路由条目则删除；
4.抑制计时器（Hold-down）：180S。当收到update时

## Slide 30: 11.3.3 Timers in RIP

## Slide 31: 11.3.4 RIP Version 2
Message format
Operation
  Support VLSM and classless addressing: subnet mask
  Authentication: Family = 0xFFFF
  Multicasting: 224.0.0.9 多播
  Encapsulation: UDP ( port 520 )
Command
Version
IP address
Subnet Mask
All 0s
Next Hop
Metric
Route Tag
Family
Notes: Family = 0xFFFF时，报文为专门的鉴别信息，16字节，同时Route tag字段被替换为鉴别类型 指明鉴别的协议
Multicasting 224.0.0.9 (all-router,全路由器)用来把报文传送给路由器，而不用包含主机

## Slide 32: Route Tag
路由标记
  To provide a method of separating "internal" RIP routes (routes for networks within the RIP routing domain) from "external" RIP routes, which may have been imported from an EGP or another IGP
N1
IR1
IR2
XR1
RIPv2
OSPF
N2, N3
Dest. | Next | Tag
N1 | IR1 | 1
N2 | IR3 | 2
N3 | IR3 | 2
IR3

## Slide 33: RFC2453 - Appendix A: Next Hop Field in a rip entry
Assume the best routes
  XR1  N1/N2; XR2  N3/N4/N5; XR3  N6/N7
XR1 exchange RIPv2 routes with IR1/IR2/IR3, setting the Next Hop field
  0.0.0.0 for N1/N2
  XR2 for N3/N4/N5
  XR3 for N6/N7
IR1
IR2
IR3
XR1
XR2
XR3
RIPv2
OSPF
Notes: Next hop指明下一跳必须发往的地址，无论是否在一个AS内

## Slide 34: Chapter 11 Routing Protocols
Interior and exterior routing
Distance vector routing & RIP
Link state routing & OSPF
Path vector routing & BGP-4

## Slide 35: 11.4 Link State Routing
Notes: 每个结点掌握全局信息，通过每个结点贡献自己的局部知识，来构建全局知识，就像共用一个地图，每个人的位置不同，走的路径也不一样

## Slide 36: 11.4 Link State Routing
Initialization初始化
  States of directed links 通过问询获取直连信息
Sharing the knowledge about the internet
  What the state of its neighborhood ( LSA )
  Where with every other router ( flooding )
  When there is a change ( event-driven )
Updating the routing table
  Dijkstra algorithm: SPF tree  Routing table
The idea —— 提供一张公路线路图！
Every router should have the whole “picture” of the internet
Notes: 拓扑必须是动态更新的，如何扩展到全局？四组动作:LSA, flooding, SPF tree  Routing table

## Slide 37: 11.4.1 Link and Link-State
Link
  A connection
Link-state
  The interface of a router and its relationship to its neighboring routers
  A directed graph（有向图）
    Vertices: routers and networks
    Edge: connect 2 router
    or connect a router to a network
Notes: 有向图，同一个链路两个方向的代价是不同的

## Slide 38
3
3
3
2
2
5
2
2
5
Metric: cost, 代价
The output side of each router interface
Ex. OSPF: 108 / bandwidth
Link state knowledge
Notes: 在一个链路状态协议中，路由器并不与其邻站交换距离信息。它采用的是每个路由器主 动地测试与其邻站相连链路的状态，将这些信息发送给它的其他邻站，而邻站将这些信息在 自治系统中传播出去

## Slide 39: 11.4.2 Flooding
LSP —— IS-IS
  Link State Packet，链路状态分组
  IS-IS
Notes: ISIS属于ISO协议簇，CONS（Connection Network Server）面向连接网络服务，CLNS（Connectionless Network Server）无连接网络服务，ISIS是无连接网络服务CLNS的一部分，用于动态路由数据包，为中间系统的路由协议，类似于IP中的OSPF；
CLNS由以下三个协议构成：CLNP：类似TCP/IP中的IP协议。IP协议为TCP/IP传输层服务。CLNP为OSI传输层服务。ISIS：中间系统的路由协议，类似于IP中的OSPF，ES-IS：主机系统与中间系统间的协议，就像IP中的ARP，ICMP等。

## Slide 40: 11.4.2 Flooding
LSP —— IS-IS
  Link State Packet，链路状态分组
  IS-IS
LSA —— OSPF
  Link State Advertisement，链路状态通告
  A Link State Update ( LSU ) packet may contain several distinct LSAs
  To reliable floods each LSA one hop further from its point of origination
Notes: ISIS属于ISO协议簇，CONS（Connection Network Server）面向连接网络服务，CLNS（Connectionless Network Server）无连接网络服务，ISIS是无连接网络服务CLNS的一部分，用于动态路由数据包，为中间系统的路由协议，类似于IP中的OSPF

## Slide 41: 11.4.2 Flooding

## Slide 42: Reliable Flooding LSA
Each newly received LSA must be acknowledged
  Explicit: Link State Acknowledgment (LSAck) packets
  Implicit: LSU packets
  Many ACKs may be grouped together into a single LSAck packet
Determining which LSA is newer, then flooding the new (and more recent) LSA out some set of the router's interfaces
  LS sequence number  LS checksum LS age
  larger larger smaller
Retransmitting LSAs until they are acknowledged
  Retransmissions interval is a configurable per-interface value
Notes: OSPF中用来与邻居交互的五个包，Hello 用来发现并维持邻居，DD 用来描述本地的LSDB信息，即和邻居互通有无，只携带LSA的Header，LSR 用于请求邻居的LSA，LSU 用于发送LSA具体信息给邻居，或者用于洪泛LSA，或者用于隐式回应LSU报文，LSAck用于回应LSU报文。

## Slide 43: 11.4.3 Dijkstra Algorithm
Calculating a tree of shortest paths with the router itself as root
Divides the nodes into 2 sets
  Tentative（临时）
  if pass the criteria
  Permanent（永久）
Notes: 收到所有的LSP后，各个结点就会有一个完整拓扑的副本，但要找到到其它所有结点的最短路径，还需要使用最短路径树SPT

## Slide 44: 11.4.3 Dijkstra Algorithm

## Slide 45: 11.4.3 Dijkstra Algorithm

## Slide 46
B
C
F
7
5
1
2
6
1
5
2
H
D
E
G
2
4
1
A
Notes: 兰色表示路径{s}

## Slide 47: SPF Algorithm Example
B
C
F
7
2
2
2
4
2
3
3
H
D
E
G
2
6
1
(2, A)
(4, B)
(8, B)
(5, B)
(6, B)
(7, B)
(9, B)
节点 | Cost | 路径 | E |  | 
B |  |  | F |  | 
C |  |  | G |  | 
D |  |  | H |  | 
2
∞
∞
∞
∞
∞
7
A-B
A-B-E
A-G
4
A-B-C
8
A-B-E-F
5
A-B-E-G
6
A-B-E-F-C
8
A-B-E-F-H
7
A-B-E-G-H
10
A
9
A-B-E-F-H-D
A-B-C-D
11
兰色表示路径{s}
Notes: 兰色表示路径{s}

## Slide 48: Build a Routing Table Based the SPF Tree
B
C
F
7
2
2
2
4
2
3
3
H
D
E
G
2
6
1
(2, A)
(4, B)
(8, B)
(5, B)
(6, B)
(7, B)
(9, B)
A
Node | Cost | Next | Node | Cost | Next
B | 2 | － | F | 5 | B
C | 8 | B | G | 6 | B
D | 9 | B | H | 7 | B
E | 4 | B |  |  | 

## Slide 49: 11.5 OSPF
Open Shortest Path First，OSPF
  v2：RFC 2328，开放最短路径优先
IP
LANs
MANs
WANs
ICMP
IGMP
ARP
RARP
Network
Layer
Network
Access Layer
TCP
UDP
Transport
Layer
OSPF
Application
Layer
89
软件实现层次
Notes: OSPF直接使用IP。也就是说，它并不使用UDP或TCP。对于IP首部的protocol字段，OSPF有其自己的值

## Slide 50: 11.5.1 Areas
Advantages
  Reduce link state advertisements overhead
  Reduce frequency of SPF calculations
  Smaller routing tables
Routing
  Intra-area routing
  Inter-area routing
Notes: 为了更加有效地处理路由选择问题，OSPF把一个自治系统划分为若干区域，洪泛仅限在area内

## Slide 51: OSPF Area
A collection of networks, hosts, and routers all contained within an AS
Autonomous System
Area 1
Area 2
Area 0 (backbone)
To
other
ASs
Notes: area，就是包含在自治系统中的一些网络、主机和路由器的集合，一个区域内的路由器使用洪泛法传送路由选择信息，区域边界有一类特殊路由器即区域边界路由器，还有一个特殊区域area 0称为主干backbone，其它所有区域必须连接到主干上

## Slide 52: Area 0
Area 2
Area 3
Area 0
Area 1
Area 0
Backbone area
  Be responsible for distributing routing information between non-backbone areas
Must be contiguous
  NOT need be physically contiguous
  Virtual link
Area 0
Area 2
Area 1
Area 3
Notes: Area 0叫做骨干区域backbone，其它所有区域必须连接到主干上，area 0中间传输的是Link State Packet，链路状态分组信息，非骨干区域之间传递的是LSA(Link State Advertisement，链路状态通告)信息，区域必须相连接，骨干和区域之间可以创建虚链路

## Slide 53: OSPF Router Types
Internal router
Backbone router
Area Border Router, ABR
AS Border Router, ASBR
Autonomous System
Area 1
Area 2
Area 0 (backbone)
To other
AS
ABR，BR
IR
ASBR，BR
IR，BR
Notes: 给每个接口指派一个无维数的费用。可以通过吞吐率、往返时间、可靠性或其他性能 来进行指派。可以给每个I P服务类型指派一个单独的费用

## Slide 54: 11.5.2 Network’s Type
Point-to-point network，点到点网络
Stub network，残桩网络
Transit network，转接网络
  Broadcast
Virtual network，虚拟网络
  NBMA
Frame Relay
X.25
Notes: 虚拟链路，两个路由器之间的链路断开时，管理员在他们之间用一条更长的路径(可能通过好几个路由器)来创建一条虚拟链路

## Slide 55: 11.5.2 Network’s Type
Notes: OSPF中网络的图形表示，3个stub network，2个transit network，2个p2p网络

## Slide 56: Transit Network: DR and BDR
Designated router & backup DR —— a true router
  指定路由器 & 备份指定路由器
Purpose
  Reduce the number of adjacencies required on a broadcast or NBMA network
  Reduce the amount of routing protocol traffic and the size of the link-state database
Example: there are N routers on a transit network
  If no DR
    Each router has ( N-1 ) neighbors
  If there is a DR
    Each non-DR has only 1 neighbor
    DR has ( N-1 ) neighbors

## Slide 57: 11.5.3 OSPF Packet Types
Notes: OSPF使用5种不同类型的分组，其中最重要的是LSA，其又分为5种

## Slide 58: 11.5.3 OSPF LSA Types
Intra-area
  Type 1: Router–LSA
  Type 2: Network–LSA
Inter-area
  Type 3: Summary–LSA
  Type 4: Summary–LSA
External
  Type 5: AS–external–LSA
Notes: 区域内 路由器/网络链路，区域间汇总链路，外部链路

## Slide 59: Intra-area LSAs
Type 1: Router–LSA
  Originated by all routers
  Describes the collected states of the router’s interfaces to an area
  Flooded throughout a single area only
Type 2: Network–LSA
  Originated for broadcast and NBMA networks by the DR
  Contains the list of routers connected to the network
  Flooded throughout a single area only
Notes: 1类LSA ，每台OSPF路由器都会产生，用来描述自身运行OSPF的接口所关联的链路状态，包括自身的router-id、接口所属的子网号、掩码，只能在本Area内泛洪扩散；2类LSA ，Network-LSA仅仅在多路访问链路上存在，由DR产生，用来描述该多路访问链路上的所有的邻居router-id，包括DR本身的router-id；
只能在本Area内泛洪扩散；

## Slide 60: Inter-area LSAs
Type 3: Summary–LSA
  Originated by ABRs
  Describes routes to networks outside the area
  Flooded throughout the LSA’s associated area
Type 4: Summary–LSA
  Originated by ABRs
  Describes routes to ASBRs
  Flooded throughout the LSA’s associated area
Notes: 汇总链路到网络，汇总链路到网络边界路由器，3类LSA Network Summary LSA，Network Summary LSA由ABR产生，用来描述本Area以外的其他OSPF Areas里的OSPF路由信息，在整个OSPF自治系统内泛洪扩散；4类LSA ASBR summary LSA，ASBR summary LSA由ABR产生，用来描述ASBR是谁，旨在告知OSPF系统内所有路由器ASBR是谁，它的内容就是ASBR的router-id，即一个32位的主机路由；在除了ASBR所在的Area的其他OSPF Areas内泛洪扩散；

## Slide 61: External LSAs
Type 5: AS–external–LSA
  Originated by ASBR
  Describes a route to a destination in another AS
  Flooded throughout the AS except the stub area
Notes: 5类LSA AS External LSA，AS External LSA由ASBR产生，用来描述OSPF自治系统之外的其他外部路由信息；

## Slide 62: OSPF LSA Example
Type 3
Default
Type 3
(Area 1)
Area 1
Area 0
Area 2
(Stub)
AS 10
AS 20
Type 2
(Area 1)
Type 5
(AS 20)
Type 4
(X=ASBR)
Type 3
(Area 1)
Type 5
(AS 20)
Type 1
(X=ASBR)
Type 3
(Area 1)
Type 1
(Area 1)
Type 1
(Area 0)
Type 3
(Area 0)
Type 5
(AS 20)
Type 4
(X=ASBR)
Type 1
(Area 0)
Type 5
(AS 20)
Type 4
(X=ASBR)
DR
Type 3
(Area 0)
Type 3
(Area 0)
Type 1
(Area 1)
Type 1
(Area 1)
Type 5
(AS 20)
Type 4
(X=ASBR)
Type 2
(Area 1)
Type 2
(Area 1)

## Slide 63: 11.5.4 OSPF Databases
Adjacency database
  All the neighbors to which a router has established bidirectional communication
  Unique for each router
Notes: Adjacency，邻接

## Slide 64: 11.5.4 OSPF Databases
Adjacency database
  All the neighbors to which a router has established bidirectional communication
  Unique for each router
Link-state database
  The relationship between each router and its neighbors
  All routers within an area have identical link-state databases
Forwarding database ( routing table )
  The routes generated when an SPF algorithm is run on the link-state database
  The routing table on each router is unique
Notes: Adjacency，邻接，

## Slide 65: 11.5.5 OSPF Packets
Format
Multicasting: 224.0.0.5, 224.0.0.6
Encapsulation: IP ( protocol 89 )
Version
Type
Router ID
Area ID
Packet Length
Authentication
Authentication
Authentication Type
Checksum
Header
OSPF Packet Data
Notes: OSPF分组格式，包括头部 和 分组数据 两部分

## Slide 66: 11.5.5 OSPF Packets
Header Format

## Slide 67: Packet Types
1: Hello packet
  A 64-byte packet sent periodically to keep a link “alive”
2: DBD ( Database Description )
  Summary contents of a router’s link-state database sent to a newly discovered neighbor
3: LSR ( Link-State Request )
  Requests more specific information about a link from a neighbor’s link-state database
4: LSU ( Link-State Update, LSA )
  Transports LSAs to neighbor routers, a reply to an LSR
5: LSAck ( Link-State Acknowledgement )
  Ack receipt of a LSA; OSPF’s routing updates are connection-oriented
Notes: OSPF中用来与邻居交互的五个包，Hello 用来发现并维持邻居，DD 用来描述本地的LSDB信息，即和邻居互通有无，只携带LSA的Header，LSR 用于请求邻居的LSA，LSU 用于发送LSA具体信息给邻居，或者用于洪泛LSA，或者用于隐式回应LSU报文，LSAck用于回应LSU报文。

## Slide 68: LSU Packet Format
OSPF common header
24 bytes, Type = 4
Repeated
LSAs
(any combination of different kinds)
# LSAs ( 1 byte )

## Slide 69: LSA Format
Header
LSA data
LS sequence number
Advertising Router ID
Link state ID
LS checksum
length
LS age
Options
LS type

## Slide 70: LSA Format

## Slide 71: Router ID
A 32-bit number assigned to each router running the OSPF protocol
  Uniquely identifies the router within an AS
  Implementation strategy: to use the largest or smallest IP interface address assigned to the router
Route ID —— in OSPF packet header
  The Router ID of the packet's source
Advertising Router ID —— in LSA header
  The Router ID of the router that originated the LSA
Notes: Route ID保证区域内唯一，实际实现中往往取路由器 IP地址最大值 或最小值的端口地址作为其Route ID，要区分源路由器ID 和 通告路由器ID

## Slide 72: Link State ID & Link ID
Link state ID —— in LSA header
Link ID —— in Router-LSA ( type 1 LSA )
LS type | Link State ID
1: router-LSA | The originating router's Router ID
2: network-LSA | The IP interface address of the network's DR
3: summary-LSA | The destination network's IP address
4: summary-LSA | The Router ID of the described ASBR
5: AS-external-LSA | The destination network's IP address
Link type | Link State ID
1: Point-to-point link | Neighbor Router ID
2: link to transit network | Interface address of DR
3: link to stub network | IP network address
4: virtual link | Neighbor Router ID
Notes: 汇总链路到网络的，为目的地网络ID； 链路类型

## Slide 73: Type1：Router–LSA
Notes: TOS数，每一条链路所宣布的服务类型数，TOS的度量 定义默认的服务类型(TOS 0)的度量值 metrics

## Slide 74: Type1： Router–LSA
Notes: 10.24.7.9

## Slide 75: Type1： Router–LSA

## Slide 76: Type2： Network–LSA
Notes: 指定路由器 代表 穿越网络来发送

## Slide 77: Type2： Network–LSA

## Slide 78: Type1&2： example
Notes: 同一个网络拓扑中，往往伴随着两类LSA

## Slide 79: Type1&2： example
Notes: 同一个网络拓扑中，往往伴随着两类LSA

## Slide 80: Type1&2： example
Notes: 同一个网络拓扑中，往往伴随着两类LSA

## Slide 81: Type3： summary-LSA

## Slide 82: Type3： summary-LSA
Notes: 一个通告只宣布一个网络，若超过1个则必须对每个网络发出单独的通过， data中只有网络掩码？ 因为网络号= route IP & mask

## Slide 83: Type4： summary-LSA ASBR
Notes: 边界路由器采用洪泛方法 传播此信息

## Slide 84: Type5： AS-external-LSA
Notes: 光到达边界路由器还是不够的，自治系统内的路由器希望知道在自治系统外的哪一个网络时可用的，需要外部链路LSA，其一个通过宣布一个网络，增加了2个字段

## Slide 85: OSPF Packet Types
Notes: OSPF使用5种不同类型的分组，其中最重要的是LSA，其又分为5种

## Slide 86: 其它分组： Hello
Notes: 优先级 有多种决策方式，如可达性，负载，无线场景中的电量等

## Slide 87: 其它分组： DBD

## Slide 88: 其它分组： DBD

## Slide 89: 其它分组： 链路状态请求

## Slide 90: 其它分组： 链路状态确认

## Slide 91: 11.5.6 OSPF Operation
1. Establish router adjacencies
  Done with the exchange of Hellos
2. Elect the DR / BDR ( if necessary )
  Done on multiaccess network only
3. Discover routes
  Done in the ExStart and Exchange states
4. Select appropriate routes
  Done through the calculation of SPF algorithm
5. Maintain routing information
  Done through the regular exchange of Hellos
Notes: 由前面的分组类型就可知道大概的OSPF时序

## Slide 92: OSPF States
Down: Not exchange information with any neighbor
Init: When an interface receives its first Hello
2-way: When it sees itself in a neighbor’s Hello
ExStart: Two neighbors use Hello to negotiate who is the “master” and who is the “slave”
Exchange: Neighbors use DBD to send each other a summary of their link-state database
Loading: Uses LSR, LSU, and LSAck to get complete link-state information
Full: Neighbors are fully adjacent

## Slide 93: Step 1. Establish router adjacencies
I am router ID 172.68.5.1 and I see no one
Down State
172.68.5.1/24
E0
172.68.5.2/24
E1
A
B
Router B 邻接表
172.68.5.1/24, int E1
Init State
I am router ID 172.68.5.2, and I see 172.68.5.1
Router A 邻接表
172.68.5.2/24, int E0
Two-way State
Hello
39547439070713
39547439070713
Hello
39547439070713
39547439070713

## Slide 94: Step 3. Discover routes
Hello Packet
A
B
Exstart
Exchange
Loading
Full
Hello Packet
DBD Packet
DBD Packet
LSAck Packet
LSAck Packet
LSR Packet
LSU Packet
LSAck Packet

## Slide 95: 11.5.7 RIP vs. OSPF
对网络拓扑的了解
路由计算方法
路由更新方式
路由更新内容
收敛速度
适用环境

## Slide 96: 11.5.7 RIP vs. OSPF
RIP协议一条路由有15跳（网关或路由器）的限制，如果一个RIP网络路由跨越超过15跳（路由器），则它认为网络不可到达，而OSPF对跨越路由器的个数没有限制。
RIP协议不是针对网络的实际情况而是定期地广播路由表，这对网络的带宽资源造成浪费，特别是大型的广域网场景中。OSPF协议的路由广播更新只发生在路由状态变化的时候，采用IP多路广播来发送链路状态更新信息，带宽利用率更高。
RIP网络是一个平面网络，对网络没有分层。OSPF在网络中建立起层次概念，在自治域中可以划分网络域，使路由的广播限制在一定的范围内，避免链路中继资源的浪费。

## Slide 97: Chapter 11 Routing Protocols
Interior and exterior routing
Distance vector routing & RIP
Link state routing & OSPF
Path vector routing & BGP-4
Notes: 当运行区域变得非常大时，前两个协议都不可操作，因为RIP跳数限制，而OSPF采用洪泛，导致通信量过大

## Slide 98: 11.6 Path Vector Routing
Path vector routing
  The AS boundary routers advertise the reachability of the networks in their own ASs to neighbor AS boundary routers
Policy routing
  Choose the best path for reaching the destination based on the value of path attributes
Notes: 路径向量， 由距离改为 路径，由自治系统内部 切换到 自治系统外部，所以RIP在AS内部，而PVR则在整个internet上

## Slide 99: Initial Routing Tables
AS 3
AS 1
AS 2
AS 4
Notes: 其内部所有网络的可达性

## Slide 100: Stabilized Routing Tables
A1
B1
C1
D1
AS1
B2
B3
B4
A4
A2
A3
A5
C2
C3
D2
D3
D4
AS2
AS3
AS4
3
3
Notes: 稳定的路由表

## Slide 101: Path Vector Routing Table
Path
  An ordered list of ASs that a packet should travel through to reach the destination
  Example
Loop prevention
Network | Next Router | Path
N01 | R01 | AS14, AS23, AS67
N02 | R05 | AS22, AS67, AS05, AS89
N03 | R06 | AS67, AS89, AS09, AS34
N04 | R12 | AS62, AS02, AS09
Notes: 途径的AS列表，对接收的可达性信息进行检查，如果接收方的AS 在到达终点所经过的AS path内，则丢弃该报文，防止出现环路

## Slide 102: Path Vector Routing Table
聚合 CIDR记法和地址聚合

## Slide 103: 11.7 BGP-4
Border Gateway Protocol，BGP
  v4：RFC 1771，RFC 1772，边界网关协议
IP
LANs
MANs
WANs
ICMP
IGMP
ARP
RARP
Network
Layer
Network
Access Layer
TCP
UDP
Transport
Layer
BGP-4
Application
Layer
179
软件实现层次

## Slide 104: 11.7.1 Types of AS
Single-homed AS
  Only one exit point to the outside
  Example: AS 1, AS 3
Multi-homed AS
  More than one exit point to the outside
  Example: AS 2
  Nontransit AS
    not allow transit traffic to pass through it
  Transit AS
    allow transit traffic to pass through it
AS 1
AS 2
R
R
R
AS 3
R
Notes: 残桩AS， 多归属AS，转接AS 允许通信量经过 如国家和国际的ISP，教材翻译版上把多归属AS和 转接AS区分为2类

## Slide 105: When to and not to Use BGP
Figure A（不用）
  A single-homed AS does NOT usually need BGP, uses default route
Figure B（可用或者可不用）
  Even if an AS has redundant paths to its ISP’s POP, BGP is NOT necessarily required
Figure C（必须用）
  An AS with redundancy to the same ISP, but different POPs still does NOT require BGP
Figure D
  An AS with multiple ISPs REQUIRES BGP
Custom
AS
ISP
AS 1
A
Custom
AS
ISP
AS 1
B
Custom
AS
ISP
AS 1
ISP
AS 1
C
Custom
AS
ISP
AS 1
ISP
AS 2
D
BGP must be used to implement
external routing policies.
Notes: 只有对多个路径要选择或者比较的时候才必须使用BGP协议（实现自治域之间的通话）

## Slide 106: 11.7.2 IBGP & EBGP Sessions
AS 1
R
AS 3
AS 2
R
R
R
R
AS 3
R
R
EBGP
EBGP
EBGP
EBGP
IBGP
IBGP
IBGP
Notes: 外部BGP 和 内部BGP会话

## Slide 107: Synchronization Rule
Example
  A BGP router (A) can not advertise routes (15.1.1.0) learned from an IBGP peer (B) to other BGP peers unless the local router (C) also has learned about the route via an IGP
AS 200
17.1.1.0
A
B
AS 100
10.1.1.0
AS 300
15.1.1.0
IBGP
Non-BGP
Router
Router C has not learned about 15.1.1.0 via an IGP
C
Notes: 同步性：只有B发送通告时，A不会向其他AS通告，直到C也发送了通告，A确保AS内所有的路由器都知道了，才会向外面进行通告

## Slide 108: 11.7.3 BGP Path Attributes
Form: < type, length, value >
Types
  Well-known mandatory
    Example: ORIGIN (1), AS_PATH (2), NEXT_HOP (3)
  Well-known discretionary
    Example: LOCAL_PREF (5), ATOMIC_AGGREGATOR (6), AGGREGATOR (7)
  Optional transitive
  Optional non-transitive
    Example: MULTI_EXIT_DISC (4)
Notes: 熟知的，路由器必须掌握， 可选的则无此要求

## Slide 109: NEXT_HOP Example
Notes: 分组必须要发送到的下一跳

## Slide 110: LOAD_PREFERENCE Example
ANET will prefer LA to the network 128.213.0.0/16

## Slide 111: MED Example
RTA will prefer RTB to the network 180.10.0.0/16

## Slide 112: 11.7.4 BGP Messages
Message header
Encapsulation
  TCP ( port 179 )  unicasting
Type（类型）
Maker（标签 标记唯一性）
（authentication or synchronization）
Length（长度）
16 bytes

## Slide 113: 11.7.4 BGP Messages

## Slide 114: Message Types
Type 1: OPEN
  Establish the peer relationship
Type 2: UPDATE
  Advertise reachable or withdrawn routes using NLRI and path attributes
  NLRI: network layer reachability information
  < length, prefix >
Type 3: NOTIFICATION
  Inform the receiving router of errors
Type 4: KEEPALIVE
  Interval keeps peer relationship
  Recommend: 1/3 Hold Time interval

## Slide 115: OPEN Messages

## Slide 116: UPDATE Messages

## Slide 117: 11.7.5 BGP Operation
Establish the BGP peer relationship
Exchange all candidate BGP routes, including withdraw routes
1.1.1.1
2.2.2.2
Net 6.0.0.0/8, 7.0.0.0/8
Net 4.0.0.0/8, 5.0.0.0/8
Net 4.0.0.0/8
Net 5.0.0.0/8
Net 6.0.0.0/8
Net 7.0.0.0/8
Net 6.0.0.0/8
Net 7.0.0.0/8
Net 4.0.0.0/8
Net 5.0.0.0/8
Withdraw 4.0.0.0/8

## Slide 118: BGP Routing Process Model
Input
Policy
Engine
Decision
Process
Routes
used by
router
Output
Policy
Engine
Routes
received
From
peers
Filtering
Attribute
manipulation
Choosing
the best
route
Routes
sent
to peers
BGP
Table
IP Routing
Table
Filtering
Attribute
manipulation

## Slide 119: 11.8 Summary
路由
  静态 vs. 动态
路由协议
  类型
    IGP：RIP、 OSPF
    EGP：BGP-4
  操作
    路由信息交换：what、 when、where
    路由计算
Notes: 最短路径 给出拓扑算出路由